## Slide 1
Future greenhouse gas emissions from metal production with implication for climate goals
The 11th Australian Conference on Life Cycle Assessment
July 20th, 2023
1National Institute of Advanced Industrial Science and Technology (AIST), Japan
2National Institute for Environmental Studies, Japan
Ryosuke YOKOI1, Takuma WATARI2, Masaharu MOTOSHITA1

## Slide 2
Climate goals and metal production
IRP (2019)
2℃ target (The Paris Agreement, 2015) → aim to limit global temperature increase below 2℃ compared to pre-industrial levels (RCP2.6)
IPCC (2014)
Reducing future GHG emissions from metal production
Metals are essential resources for decarbonization → At the same time, their production accounts for 10% of global greenhouse gas (GHG) emissions
Metal demand will increase due to population and economic growth and decarbonization technology.
Concerns for limitation of future metal use

## Slide 3
Future metal demand projection - How will metal demand change due to population and economic growth under different socio-economic scenarios?
Future GHG emissions from metal production - Can we achieve the climate goal for metal production? - Which measures will be effective to reduce GHG emissions from metal production?
*Analysis was conducted for six metals → Aluminum, Copper, Iron, Lead, Nickel, Zinc
Purposes

## Slide 4
Methods (overview)
SSPs*
Population, GDP, Energy mix
GHG emissions from metal production(2010-2100)
[Al, Cu, Fe, Pb, Ni, Zn]
Historical in-use metal stocks for each countries
Watari and Yokoi, Resour. Policy, 2021
*Shared Socioeconomic pathways
Logistic curve modelling
Future demand
Material flow analysis
Primary/Secondary metal production
Recycling rate
Lifetime
Yield rate
Previous study
GHG emission intensity
Life cycle assessment
Van der Voet et al., J. Ind. Ecol., 2018
Scenario analysis
Climate goal (RCP2.6_Industrial sector)
Comparison

## Slide 5
Metal stock per capita do not increase infinitely but will eventually saturate at a certain level
Developing countries will follow the stock growth patterns of developed countries
Low income
High income
Upper Middle income
Lower Middle income
Waste management
<Stock saturation approach>
Project future metal stock growth → Calculate future metal demand
Production (primary/secondary)
Landfill
Use (metal stock)
Extraction
Recycling
Approach (future metal demand projection)

## Slide 6
Future scenarios that provide quantitative and qualitative description of future socio-economic situations
Electricity mix
Population
Economic growth (GDP)
*Shared Socio-economic Pathways (SSPs)

## Slide 7
Population and economic growth lead to significant increase in demand (larger than the current level throughout 21st century) (maximum by 2.3–4.4 times)
Different trends among SSPs → Peak until 2050 and then decline (SSP1, 5), continue to increase (SSP3)
(Yokoi et al. 2022)
Future metal demand

## Slide 8
Increasing metal stocks (waste flow) increase recycling, leading to decrease in mine production
Different trends among metals → Stock growth pattern, recycling rate
Future mine production

## Slide 9
Further efforts are required to achieve the climate goal
GHG emissions from metal production
GHG emissions is mainly attributed to iron production (the share will decrease)
Increase in GHG emissions especially in the early century driven by population and economic growth in middle-income countries.
SSPs have a great effect on GHG emissions, but no SSP can achieve the climate goal

## Slide 10
Metal use level
Product lifetime
GHG emission intensity
Recycling rate
Saturation value of stock per capita
Improving a single parameter is insufficient to achieve the climate goal
Sustainable socio-economic pathway and multiple measures are essential
How can we reduce GHG emissions from metal production?
Improving recycling rate will be effective in the long-term
Improving all parameters will be required
Emission intensity and metal use level can be key factors
Can we improve these parameters?

## Slide 11
Should we go back to the past level?
Per capita metal stock level in high-income level countries (iron)
-10%→2002 (9.6 ton), -20%→1993 (8.5 ton), -30%→1980 (7.5 ton)
Consumer behavior
Living standard
Per capita service demand
Utilizing underused infrastructure and buildings
Sharing economy
Product service systems
Weight saving
Material substitution
Stock productivity (reciprocal)
Service utilization rate (reciprocal)
Lifestyle, Living standard
Technological improvement
Systematic improvement
Reducing metal use level (stock level)

## Slide 12
Prompt actions are essential
Energy transition is not enough because GHG emissions are mainly due to reduction process with coke
BF-BOF: Blast furnace-basic oxygen furnace CCUS: Carbon dioxide capture, utilization and storage
Hydrogen reduction
BF-BOF + CCUS
Increase in GHG emissions especially in the early century
Reducing emission intensity of primary iron production
<Emission intensity of primary iron production>

## Slide 13
Socio-economic pathways (SSPs) have a great effect on GHG emissions → However, no SSP will achieve the climate goal (2℃ target) for metal production
Energy transition is effective but will be insufficient for achieving the climate goal → For primary iron production, additional technological development (e.g., hydrogen reduction, CCUS) is required
In addition to following the sustainable socio-economic pathway, implementing multiple measures immediately with international cooperation is essential
Future GHG emissions from metal production
Population and economic growth will cause significant increase in metal demand and mine production
Future demand projection for six metals (Al, Cu, Fe, Pb, Ni, Zn)
Summary
Yokoi, R., Watari, T., Motoshita, M., 2022. Future greenhouse gas emissions from metal production: gaps and opportunities towards climate goals. Energy Environ. Sci. 15, 146–157.